Report of RFTech presentation during

Mixdes conference

(June 26-27, Wroclaw, Poland)

Title of presentation:

PCIExpress Hot-Plug Mechanism in Linux-based ATCA Control Systems

Presenter:

Adam Piotrowski (PhD student)

Department of Microelectronics and Computer Science

Technical University of Lodz

Lodz, Poland

email: komam@dmcs.pl

A. Piotrowski presented an overview of PCIExpress Hot-Plug mechanism and its implementation in kernel of Linux operating system.  The problem with cooperation between FPGA-based PCIExpress endpoints and Hot-Plug was discussed. Additionally, example system that allows to connect uDev device manager with user application to check correctness of loaded firmware was presented.

Abstract: PCI Express architecture is a widely used communication bus designed for industrial application. Additionally, 	according to PICMG 3.4 specification it is a part of ATCA architecture. One of the features offered by PCI Express standard is possibility of replacing the system components without shutting down entire system. In this paper, authors present general overview of Hot-Plug implementation in Linux operating system used in ATCA carrier board.

Index Term: PCIExpress, Hot-Plug, ATCA, Advanced Telecommunications Computing Architecture, AdvancedTCA, Linux

Remarks:

During the conference author was able to discuss presented solutions with people directly involved in  development of ATCA-based systems with implemented PCIExpress bus.

We acknowledge funding from the European Commission under the FP7 Research Infrastructures project EuCARD, grant agreement no. 227579.