## Slide 1: Machine Progress Towards Higher Luminosity
Frank Zimmermann
CMS Upgrade Meeting
FNAL, Chicago, 7 November 2011 (via EVO)
Thanks to Martin Aleksa, Gianluigi Arduini, Ralph Assmann, Hannes Bartosik, Oliver Brüning, Octavio Dominguez, Massimiliano Ferro-Luzzi, Humberto Maury, Jordan Nash, Yannis Papaphilippou, Anders Ryd, Benoit Salvant

## Slide 2: topics
luminosity evolution over next few years
in light of 2011 experience
- beam-beam limits
- b* reach (aperture, collimation, optics)
- leveling, pile up
50-ns vs 25-ns running
- electron cloud
- enhanced satellites w 50 ns spacing
before/after Linac4 & other upgrades
how to reach highest luminosity?

## Slide 3
2011 peak luminosity evolution
peak luminosity increased almost linearly over the year (adding more
bunches, increasing bunch intensity, reducing b*) – now near the limit

## Slide 4
~1.5/fb
/month
~1/fb
/month
9 months with ~26 days each & peak luminosity of 3.6x1033 cm-2s-1
(at the end) and 5.5/fb in total gives a “Hübner factor” of ~0.08
2011 integrated luminosity evolution

## Slide 5: 2011 LHC records
 | CMS | ATLAS
peak stable luminosity delivered | 3.55x1033 cm-2 s-1 | 3.65x1033 cm-2 s-1
maximum luminosity in on fill | 123.13 pb-1 | 122.44 pb-1
maximum luminosity in one day | 135.65 pb-1 | 135.45 pb-1
maximum luminosity in 7 days | 537.9 pb-1 | 583.5 pb-1
maximum luminosity in 1 month | 1614.99 pb-1 | 
maximum colliding bunches (w/o satellites) | 1331 | 1331
maximum peak #events /crossing |  | 23.8 (33.96)
maximum (av.) #events / bunch crossing | 19.94 | 17.5 (32.21)
longest time in stable beams for one fill | 26 h | 26 h
longest time in stable beams for one day | 19.9 h (82.9%) | 21.9 h (91.2%)
longest time in stable beams for one week | 107.1 h (63.7%)? | 107.1 h (63.7%)
longest time in stable beams for one month | 232.2 h | 232.2 h?
fastest turnaround to stable beams | 2.1 h | 2.1 h

## Slide 6
2011 time spent in physics
1400/(31 24 8) ~23.5% of the total,
+ lumi decay + lumi ramp up → consistent with Hübner factor 0.08

## Slide 7: 2011 time spent in physics

## Slide 8
2011 length of physics fills

## Slide 9: 10 year plan 2011-2021
2022
LS3
Installation of the HL-LHC hardware
p-Pb
run
4 TeV?
6.5 TeV?
from early 2011

## Slide 10
 | design | October 2011 | end 2012 ? | 2016 ??
Beam energy | 7 TeV | 3.5 TeV | 4 TeV | 6.5 TeV
transv. norm. emittance | 3.75 mm | 2.5 mm | 2.5 mm | 3.5 mm
beta* | 0.55 m | 1.0 m | 0.7 m | 0.5 m
IP beam size | 16.7 mm | 24 mm | 19 mm | 17 mm
bunch intensity | 1.15x1011 | 1.5x1011 | 1.6x1011 | 1.2x1011
# colliding bunches | 2808 | 1331 | 1350 | 2800
bunch spacing | 25 ns | 50 ns | 50 ns | 25 ns
beam current | 0.582 A | 0.335 A | 0.388 A | 0.604 A
rms bunch length | 7.55 cm | 9 cm | 9 cm | 7.6 cm
full crossing angle | 285 mrad | 240 mrad | 240 mrad | 260 mrad
“Piwinski angle” | 0.64 | 0.37 | 0.51 | 0.61
peak luminosity | 1034 cm-2s-1 | 3.6x1033 cm-2s-1 | 7.4x1033 cm-2s-1 | 1.3x1034 cm-2s-1
average peak pile up* | 25 | 18 | 36 | 30
LHC beam parameters
* with s~80 mbarn

## Slide 11: 10-year luminosity forecast
modified from O. Brüning, M. Lamont, L. Rossi
6.5 TeV &
transition
to 25 ns
total
17 fb-1
total
156 fb-1
total
~400 fb-1

## Slide 12
10-year luminosity forecast
HL-LHC
modified from O. Brüning, M. Lamont, L. Rossi

## Slide 13
10-year pile-up forecast

## Slide 14: 2011: offset leveling test
conclusion: the luminosity can be successfully leveled using transverse offsets between 0 and a few s (here at IP8) without significant effects on the beam or the performance of the other experiments (IP1&5)
W. Herr et al,
March 2011

## Slide 15: Monday 30/5 to Wednesday 08/06
Beam intensities
Luminosities
1.4e11
1.2e33
Wk 3
Blow up
leveling works
2011: routine leveling in IP2 & 8
3e32

## Slide 16: enhanced satellites for ALICE
wall current profile SPS beam
average over sequential 10 turns, 20 ms before extraction
144 bunches with satellites
T.Bohl, S.Hancock
Satellites going up to about 8 %, average of few %
test in week 43
enhanced
satellites
are produced
by RF
gymnastics
in the PS
(S. Hancock)
R. Assmann, LMC

## Slide 17
T. Pieloni, W. Herr et al, May 2011
beam parameters investigated beyond nominal LHC (Nb = 1.8‐1.95x1011, ε =1.2-1.4 μm); no significant beam losses nor emittance effects observed with linear head-on parameter of ξbb= 0.02 /IP and ξbb=0.034 (total) – more than 3x above design!
>0.03
no head-on beam-beam limit found yet

## Slide 18: high pile-up test – CMS results
A. Ryd, LMC112
no “pile-up limit” found yet

## Slide 19: long-range beam-beam effect
40%
35%
50%
30%
HD 2-8
Small LR
HD 1-5
Strong LR
HD 1-2-5
Strong LR
HD 8
Tiny LR
crossing angle
100% = 240 mrad
at b*=1.5 m
50-ns spacing
W. Herr et al, August 2011
we cannot reduce the crossing angle
much below 240 mrad at b*=1 m

## Slide 20: b* reach from 2011 MDs
R. Assmann et al, CERN-ATS-Note-2011-079 MD
tight collimator settings tested in MD block2
“We found a good IR aperture in both planes and IPs. So good that we want to take more time to see if we overlooked something. Had to open the TCT aperture to the following values before seeing primary losses at the triplet:” IR1 - V -> 18.3 - 18.8 s (at b*=1.5 m) IR1 - H -> 19.8 - 20.3 s IR5 - V -> ≥ 20.3 s (corrector limit reached) IR5 - H -> 19.8 - 20.3 s S. Redaelli, M. Giovannozzi et al
LHC MD block 3
tight collimator settings
with TCT at 9.3 s
qualified for physics
operation
at present TCTs at 11.8 s at b*=1 m; this could be reduced to 9.3 s
(b*<0.7 m)

## Slide 21: 2011: LHC emittance vs bunch intensity with 50 ns spacing
G. Arduini, LMC110
at Nb=1.5x1011
emittance is
about
~2.5 mm

## Slide 22
2011: injector emittance vs equivalent LHC bunch intensity (w/o losses)
G. Arduini, LMC110

## Slide 23: 50 ns vs 25 ns
50-ns beam: smaller emittance from the PS (less splittings in the PS; i.e. less charge in the PSB); ~2 mm vs ~3.5 mm at LHC injection
25-ns beam: emittance growth due to e-cloud in the SPS and LHC (to be improved by scrubbing in the LHC, and a-C coating in the SPS)
25-ns has more long-range collisions
total current limit (by vacuum; RF) → limit # bunches
bunch train current limits in SPS & LHC → limit # bunches
UFO rate seems to greatly increase for 25-ns spacing
ultimately (2014?) we must (try to) transit to 25-ns spacing because of pile up
also there are the possibilities to alternate high-luminosity high-pile-up 50-ns running and lower-luminosity 25-ns running with reduced pile up (?); or to use ALICE enhanced satellites to get both high and low pile up events at the same time – preferences of experiments?

## Slide 24: e-cloud emittance blow up with 25 ns MD October 2011
2 mm
3.5 mm

## Slide 25
electron cloud scrubbing – LHC arcs
of low-energy e-
after April
2011 scrubbing run
H. Maury
25-ns tests
October 2011
goal for 25 ns

## Slide 26
possible concerns for 2014/15
radiation to electronics – SEU’s
UFOs at higher energy & with 25 ns
electron cloud & high energy & at 25 ns
emittance growth in physics
…

## Slide 27
Duoplasmatron = Source  90 keV (kinetic energy)
LINAC2 = Linear accelerator  50 MeV
PSBooster = Proton Synchrotron Booster  1.4 GeV
PS = Proton Synchrotron  25 GeV
SPS = Super Proton Synchrotron  450 GeV
LHC = Large Hadron Collider  7 TeV
LHC injector complex

## Slide 28: 3 LHC p beams from the CERN PS
 | Possible Characteristics 2011 |  |  |  |  |  |  |  |  |  | 
 | PSB extraction |  |  |  | PS extraction |  |  | SPS extraction |  |  | 
 | Ip / ring | ɛh and ɛv | nb | nb | Ip / bunch | ɛh and ɛv | nb | Ip / bunch | ɛh and ɛv | ɛlongit | nb
 | [x1011] | [mm ∙ mrad] | batches | bunches | [x1011] | [mm ∙ mrad] | bunches | [x1011] | [mm ∙ mrad] | [eVs] | bunches
 |  | 1σ, norm. |  |  |  | 1σ, norm. |  |  | 1σ, norm. |  | 
LHC25 (DB) | 16 | 2.5 | 2 | 4 + 2 | 1.3 | 2.5 | 72 | 1.15 | 3.6 | 0.7 | 4 x 72
LHC50 (SB) | 24 | 3.5 | 1 | 3 x 2 | 1.75 | 3.5 | 36 | 1.45 | <3.5 | ≤ 0.8 | 4 x 36
LHC50 (DB) | 8 | 1.2 | 2 | 4 + 2 | 1.3 | 1.3 | 36 | 1.15 (?) | 1.5 (?) | ≤ 0.8 | 4 x 36
Ɛh/v very low, potential for higher than nominal intensity
25 ns beam from the PS
50 ns beam from the PS
Rende
Steerenberg
Chamonix
2011
LHC50 SB (2010) → LHC 50 DB (low emittance, 2011) or LHC25 DB (more bunches)
+ future PS “batch compression” to (further) boost the brightness?

## Slide 29: SPS: 50ns bunch train – Double PSB batch
  Intensity 1.65 1011 p/b reached !
    Up to 4 batches injected
    Very low losses along the cycle (reproducible 3%)
    ex=2.0 mm and ey=1.9 mm at flat top (sum 3.9)
Roland Garoby, LHCC 14/06/2011
May 2011

## Slide 30: new optics for SPS (low γt or “Q20”)
Slippage factor in SPS relative to nominal optics
1978
2010
1998
nominal
SPS intensity limitations for LHC p beams in SPS
  TMCI due to transverse impedance, Nth ~ η
  Loss of longitudinal Landau damping), Nth ~ ε2τη
  Longitudinal coupled bunch instabilities, Nth ~ ηε2/τ
  Electron cloud instability
Slippage factor η defined by optics through transition energy (γt):
Increase in instability thresholds Nth for higher slippage factor η due to faster synchrotron motion ( ) and faster damping of instabilities
Nth … Instability threshold
ε … longitudinal emittance
τ … bunch length
η … slippage factor
Low γt optics
Nominal optics
H. Bartosik, Y. Papaphilippou
not yet fully commissioned for LHC
Notes: TMCI threshold can be increased by increasing chromaticity or longitudinal emittance

## Slide 31: SPS single-bunch intensity limits (units of protons/bunch)
Benoit Salvant
chromaticity Q’/Q | 0.0 | 0.07
old Q26 optics | 1.7x1011 | 2.2 x1011
new Q20 optics | 2.8x1011 | 3.8 x1011
>2 x LHC
ultimate

## Slide 32: Nb & e with SPS Q20 low-gt optics (1 bunch)
extracted intensity together with total losses along the cycle
overestimation of horizontal emittance and its slope (dependence of dp/p on intensity)
PSB emittances: ~ 1μm < 1.5e11p / ~ 1.1μm @ 2e11p / ~ 1.3μm @ 3e11p
bunch length slightly increasing with intensity
up to Nb~3x1011 (~3x LHC at 450 GeV with ge~2.5 mm (2/3 LHC design!)
Hannes Bartosik
11 May 2011
intensity
emittance
measured!

## Slide 33: Overall LHC Injector Upgrade Planning
 | Linac4 | PS injector, PS and SPS | Beam characteristics at LHC injection
2011 - 2012 | Continuation of construction… | Beam studies § simulations Investigation of RCS option Hardware prototyping Design § construction of some equipment TDR | 25 ns, 1.2 1011p/b, ~2.5 mm.mrad 50 ns, 1.7 1011p/b, ~2.2 mm.mrad 75 ns, 1.2 1011 p/b, £ 2 mm.mrad
2013 – 2014 (Long Shutdown 1) | Linac4 beam commissioning Connection to PSB ? | PSB modification (H- injection) ? PSB beam commissioning ? Modifications and installation of prototypes in PS and SPS | 
2015 - 2017 | Progressive increase of Linac4 beam current | If Linac4 connected: progressive increase of PSB brightness Some improvement of PS beam (Injection still at 1.4 GeV) Equipment design § construction for PS injector, PS and SPS Beam studies | Limited gain at LHC injection (pending PSB (or RCS), PS and SPS hardware upgrades)
2018 (Long Shutdown 2) |  | Extensive installations in PS injector, PS and SPS Beam commissioning | 
2019 –2021 |  |  | After ~1 year of operation: beam characteristics for HL-LHC…
R. Garoby, 24 June 2011

## Slide 34: Linac4 commissioning schedule
Start of beam commissioning (3MeV): May 2013
End of beam commissioning (160 MeV): April 2014
(version November 2010)
5 commissioning stages:
(on intermediate dumps)
3 MeV
10 MeV
50 MeV
100 MeV
160 MeV
Linac4 ready : April 2014
M. Vretenar, CERN MAC, August 2011

## Slide 35: Baseline scenario: LINAC4 connection in LS2
Keep Linac4 commissioning schedule (April 2014)
Schedule connection to the PSB only in LS2 → minimum risk; but need to operate in parallel Linac2 and Linac4 for some years;
In case of problems with Linac2, be ready from 2015 to an “emergency” connection of Linac4, with 2 possible options:
a) with H- & full performance after 7-month shutdown;
b) with protons at 50 MeV after a few days shutdown but with reduced PSB performance.
M. Vretenar, CERN MAC, August 2011

## Slide 36: alternative LINAC4 connection scenarios for LS1 (NOT baseline)
+ : Linac4 + PSB available from 2015 (PSB performance + mitigate risk of Linac2 failure)
- : a) Start LHC only in 2015
b) Injectors have to stop in 2014.
A.
“green light” Jan. 2014, Linac4 commissioned only to 100 MeV
B.
“green light” June 2015, Linac4 commissioned + 5 months reliability run
+ : Linac4 + PSB available from 2015 (PSB performance + mitigate risk of Linac2 failure)
- : a) Risk of reliability/performance issues appearing in the last phase of commissioning
b) Injectors have to stop in 2014.
M. Vretenar, CERN MAC, August 2011

## Slide 37: would there be any benefit for LHC from Linac4 alone?
For 25 ns spacing it is very difficult to go beyond what is done today without RF & e-cloud improvements in the SPS & PSB energy upgrade (all planned in LS2)
With 50 ns bunch spacing one might gain up to a factor of 2 in intensity at the SPS from LINAC4
R. Garoby, CERN MAC, August 2011

## Slide 38: potential 50-ns luminosity reach with LINAC4 (my estimate)
ge ~2.5 mm
Nb ~2.5x1011
E= 4 TeV, b*~0.7 m:
L~1.6x1034 cm-2s-1, pile up ~74
E = 6.5 TeV, b*~0.45 m :
L~3.7x1034 cm-2s-1, pile up ~170

## Slide 39: a few conclusions
in 2012 may expect addtitonal 10/fb at 4 TeV with ~36 maximum pile up at 50 ns spacing
from 2014 run with 25 ns spacing at 6.5 TeV
by 2017 may have ~150/fb and by 2021 ~400/fb with maximum pile up <50
early connection of LINAC4 might (only) help for 50-ns operation, but could then give highest luminosity & with high maximum pile up (70-170)
maximum luminosity is determined by acceptable pile up (no head-on beam-beam limit!)
leveling could also be applied for CMS to limit the pile up
enhanced satellites would give low & high pile up events
LHC will exceed design luminosity; 2021: time for HL-LHC

## Slide 40: thank you for your attention