## Slide 1: HIGH ENERGY LHC
E. Todesco
CERN, Geneva Switzerland
On behalf of the HE-LHC working group
R. Assmann, R. Bailey, O. Bruning, O. Dominguez Sanchez, G. De Rijk, M. Jimenez, S. Myers, L. Rossi, L. Tavian, E. Todesco, F. Zimmermann « First thoughts on a Higher Energy LHC » CERN ATS-2010-177
and of the participants to the Malta workshop
Paris, 11th May 2011
2nd EuCard meeting

## Slide 2: A 16.5+16.5 TeV proton collider in the LHC TUNNEL
The idea
  Installing a 16.5+16.5 TeV proton
  accelerator in the LEP tunnel
  Main ingredient: 20 T operational field dipoles
    Proposal in 2005 for an LHC tripler, with 24 T magnets [P. McIntyre, A. Sattarov, “On the feasibility of a tripler upgrade for the LHC”, PAC (2005) 634].
Working group launched at CERN in May 2010
  www.cern.ch/he-lhc
  Report published in September R. Assmann, R. Bailey, O. Bruning, O. Dominguez Sanchez, G. De Rijk, M. Jimenez, S. Myers, L. Rossi, L. Tavian, E. Todesco, F. Zimmermann « First thoughts on a Higher Energy LHC » CERN ATS-2010-177
Workshop in Malta October 2010
  http://indico.cern.ch/internalPage.py?pageId=0&confId=97971
  Proceedings: CERN Yellow report 2011-3

## Slide 3: THE VIEW FROM THE HIGH ENERGY PHYSICS COMMUNITY
Discovery potential [J. Wells, CERN 2011-3]
  The panorama is complex and LHC discoveries will shed more light but …
  The energy frontier is always extremely interesting and for many processes cannot be traded with more luminosity at lower energy
Do we need new experiments ? [M. Nessi, CERN 2011-3]
  Most of the electronics and inner detectors will be rebuild and upgraded already for the HL-LHC – so it will be for the HE-LHC
    Modular and gradual approach is possible
  Main questions to be answered ‘soon’ (in a few years)
    Can we manage to keep the same magnets and structures, just replacing modules?
    If a new detector is needed, will it involve new civil engineering?
The results of the LHC will change everything, one way or another. There will be a new “theory of the day” at each major discovery, and the arguments will sharpen in some ways and become more divergent in other ways. Yet, the need to explore the high energy frontier will remain.

## Slide 4: THE INJECTION ENERGY
Injection energy is important
  Keeping the same injection would avoid the need of new injectors and transfer lines but would bring the dynamic range from 15.6 to more than 40 – not considered as realistic
  Injection at 1.2 TeV (or more) we keep the same dynamic range
  Beneficial effect on the aperture
    2/3 of LHC aperture used by the beam
    Higher injection energy  lower beam size √E  40 mm aperture possible
  Aperture is very valuable asset – keep it as low as possible
    Reduction from 56 mm to 40 mm allows 20% reduction of the cost and 30% less stored energy (with a coil of 80 mm thickness)

## Slide 5: Peak LUMINOSITY
Luminosity: twice the LHC
  A factor 2.4 comes for free (nearly …) from the energy
  Proposal of rebalancing: 50% less bunches nb compensated by 15% larger bunch intensity N and 30% smaller b*
     Electron cloud becomes less critical (larger bunch spacing: 50 ns)
     Smaller stored energy (not 2.4 the LHC, but only 30% more)
     Smaller load due to synchrotron radiation (not 2.4^4=31 LHC, but only 17 LHC)
    The smaller b* and the larger intensity seem at hand
Luminosity parameters [F. Zimmermann et al. CERN 20111-3]

## Slide 6: INTEGRATED LUMINOSITY AND SYNCHROTRON RADIATION
Luminosity: twice the LHC
  Synchrotron radiation induces a strong reduction of emittance
    Artificial transverse emittance blow-up can be needed to avoid reaching beam-beam limit
    Optimal running time of the order of 10 h (still reasonable)
    One should get about 0.8 fb-1 per day
Evolution of luminosity during a run [F. Zimmermann et al. CERN 20111-3]

## Slide 7: SYNCHROTRON RADIATION AND HEAT LOADS
Synchrotron radiation: scaled with 4th power of the energy
  But we have less beam, so SR power is a factor 17 larger
  Less than 2.4^4= 31,
  but still large
Heat loads
  The term coming from synchrotron radiation is dominant – on the beam screen we have 6 times larger loads than in the LHC
    Different options of beam screen temperature: 40-60 K is appealing
  Cold mass heat load is only 50% larger (related to MB current)
Not yet possible to tell is LHC cryogenics can be reused
  It will be 20 years old, but …
Heat loads in the LHC and one option for HE LHC [D. Delikaris, L. Tavian CERN 2011-3]

## Slide 8: BEAM SCREEN, INJECTION, DUMP
Magneto resistance of the beam screen: increase of about a factor 2 w.r.t. LHC (due to higher field) [E. Metral, CERN 2011-3]
  Impedances scale with √ of magneto resistance  40% larger impedance should not be an issue for the beam stability
Injection lines (in case of injection at 1.3 TeV) [B. Goddard et al. , CERN 2011-3]
  Completely new layout needed – more space needed (60 m between quads) also for injection protection devices
Dump [B. Goddard et al. , CERN 2011-3]
  Dump possible with a similar layout as in the LHC – upgrade of dilution or of the dumping block needed

## Slide 9: INJECTORS
Option for the injectors [R. Garoby, CERN 2011-3]
  Low Energy Ring (LER) in the LHC tunnel:
  2 T superferric dipoles
    Option1 – bypass of experiments
    Option2 – going through experiments
    Injection in one go
    No additional work for transfer lines
  Superconducting SPS (S-SPS): 5-6 T dipoles
    Not occupying precious space in the
    LHC tunnel
    No problem of experiments bypass
    Higher cost
  Issue: LHC injectors still working in 2025-2040?
LER magnets [H. Piekartz, CERN 2011-3]
HE-LHC and LER in the LEP tunnel
[H. Piekartz, CERN 2011-3]

## Slide 10: PROTECTION AND COLLIMATION
Several aspects to be considered
  Efficiency: degraded by factor 3-6 w.r.t. LHC – will be addressed by with future upgrades
  Robustness: energy density a factor 2.6 larger than acceptable
    Either larger emittance, or more robust materials, or review of limits
  Larger apertures at 16.5 TeV to avoid too small gaps and large impedance
Stored energy vs beam energy (left) and energy density versus beam energy (right) [R. Assman. CERN 2011-3]

## Slide 11: MAGNETS: DIPOLES MAIN CONSTRAINTS
Design is driven by
  Transverse space in the tunnel  transverse size of the magnet
    570 mm diameter for the cold mass in the LHC
    We assume 800 mm diameter for the HE-LHC
    Coil must be reasonably compact
  Cost: we need Nb3Sn and HTS
    Cost of Nb3Sn ~4 times Nb-Ti
    Cost of HTS ~ 4 times Nb3Sn
     grading of material is necessary
  Margin
    We ask to work with 20% margin
    from critical surface, i.e., we have
    to design a magnet for 25 T
    LHC ‘Energy Upgrade’ proposed in [O. Bruning, et al.,LHC Project Report 626 (2002)]
    24 T dipole for LHC tripler proposed in [P. McIntyre, A. Sattarov, PAC 2005, 634]
    This proposal: [L. Rossi, E. Todesco, CERN 2011-3]

## Slide 12: MAGNETS: DIPOLE COIL
First choice: current density – keep the same as the LHC
  B [T] ~ 0.0007 × coil width [mm] × current density [A/mm2]
  LHC: 8 [T]~ 0.0007 × 30 × 380
  Accelerators used current density of the order of 350400 A/mm2
    This provides ~2.5 T for 10 mm thickness
    80 mm needed for reaching 20 T
  w.r.t. McIntyre design at 800 A/mm2
    Stress increases only by 2.4
    Coil size is still manageable
Operational field versus coil width in accelerator magnets

## Slide 13: MAGNETS: DIPOLE PARAMTERS
Stored energy is critical
Stress in the coil at 20 T operational field [A. Milanese]
Sketch of the double aperture magnet
with the iron yoke – Coils are in blue
Coil grading (one quarter of coil shown)

## Slide 14: COST
Acrobatic estimate (prices for 2025 …)
  Nb3Sn 4 times more expensive than Nb-Ti
  HTS 4 times more expensive than Nb3Sn
3.8 M$ of conductor per LHC-like magnet (15 m, 2-in-1)
  4.6 M$ including manufacturing (hypothesis: the same as LHC except coil construction increased by 50%)
1200 dipoles → 5500 M$
  About five times the LHC for 2.5 times the field

## Slide 15: THE NEW TUNNEL OPTION
Option 1:
  3000 LHC magnets at 8.3 T (no HTS no Nb3Sn) in 52 km tunnel
  Magnet cost: 3000 M$
Option 2:
  1600 magnets with NB-Ti and Nb3Sn at 15 T (no HTS) in a 33 km tunnel
  Magnet cost: 4200 M$
Plus
  Tunnel cost
  Infrastructures, which can be as costly as the tunnel
  Experiments
  Permits for sites, …

## Slide 16: CONCLUSIONS
From a point of view of beam dynamics, the HE-LHC does not present hard showstoppers
The main challenge is the 20 T magnet
  Available technology today is up to 15 T
  Cost
  Stored energy and protection
Main critical choices
  Timeline for R&D on magnets
  20 T or 15 T ?
  Injector options
  Can we use the experiments layouts with upgrade of detectors?

## Slide 17: RESERVE SLIDES

## Slide 18: GUIDELINES FOR THE COIL
What material can tolerate 380 A/mm2 and at what field ?
  For Nb-Ti: LHC performances - up to 8 T
  For Nb3Sn: 1500 A/mm2 at 15 T, 4.2 K – up to 12 T
    With lower current density 190 A/mm2/m we can get to 15 T
  Last 5 T made by HTS - we ask for having ~380 A/mm2
    Today in Bi-2212 we have half, i.e., ~200 A/mm2
Engineering current density versus field for Nb-Ti and Nb3Sn (lines)
and operational current (markers)

## Slide 19: Main OPEN ISSUES
HTS
  Critical current: reach 400 A/mm2 operational current in HTS
    With 200 A/mm2 as today, one would reach ~17.5 T
  Manufacturing of dipoles
    We start to have experience on solenoids, much less on dipoles
Building an hybrid coil
  Different curing for Nb-Ti, Nb3Sn, HTS
Protection
  Very large stored energy
  Hybrid coil
Stresses
  200 MPa are at the limit of Nb3Sn