## Slide 1: The Future of Highest-Energy Accelerators
Frank Zimmermann
CERN, Geneva, Switzerland
Work supported by the European Commission under the FP7 Research Infrastructures project EuCARD, grant agreement no.~227579
thanks to Y. Cai, A. Bogacz, O. Brüning,
D. Douglas, W. Fischer, M. Furman, Z. Huang, T. Roser, W. Scandale, V. Shiltsev, R. Tomas

## Slide 2
The most important tool in this story was the particle accelerator!
Higgs boson
spin=0
A. Caldwell, March 2012

## Slide 3
28 Nobel Prizes for particle physics
include several for accelerator-
based experiments performed at SLAC

## Slide 4
particle colliders over the decades
V. Shiltsev,
Physics-Uspekhi, 2012

## Slide 5
peak luminosities of particle colliders
L= (event rate) / (cross section)
V. Shiltsev,
Physics-Uspekhi, 2012

## Slide 6
Table-top cyclotron. | 
“Dr Livingston has asked me to advise you that he has obtained 1,100,000 volt protons. He also suggested that I add ‘Whoopee’!”
—Telegram to Lawrence, 3 August 1931
1st cyclotron by
Ernest O. Lawrence
& Stanley Livingston
~1930
diameter 4.5 inches
(~11 cm)
final proton energy
1.1 MeV

## Slide 7
1st cyclotron, ~1930
E.O. Lawrence
11-cm diameter
1.1 MeV protons
Large Hadron
Collider (LHC), 2008,
9-km diameter
7 TeV protons
after ~80 years
~107 x more energy
~105 x larger

## Slide 8: hadron colliders
“discovery machines” (hadrons: composite particles)
W and Z bosons, top quark, Higgs boson
next: supersymmetry, dark matter, extra dimensions, dark energy,…?
maximum energy
Emax≈ e c B r
magnetic field
LHC: superconduncting magnets (Nb-Ti) with B≈8.33 T
bending radius
LHC: r≈3 km

## Slide 9: higher-energy hadron colliders
stronger magnetic fields:
  Nb-Ti (~8 T) → Nb3Sn (~15 T) → HTS (~20 T)
  factor 2.5 in beam energy (“HE-LHC”)
larger circumference:
  27 km (LHC) → 80 km (“VHE-LHC”?)
  another factor 3 in beam energy
  combined: an order of magnitude in energy

## Slide 10: pushing SC magnet technology
Bi-2212: only round-wire superconductor at fields > 18 T
P. McIntyre et al, Proc. EuCARD-AccNet workshop HE-LHC10, Malta, Oct. 2010, Yellow Report CERN-2011-003
P. Lee, Compilation of current je data, http://www.magnet.fsu.edu/magnettechnology/research/asc/plots.html
Nb-Ti ~8 T
(LHC, 2005)
→
Nb3Sn ~15-17 T
(HL-LHC, 2022)
→
Bi-2212 ~20-24 T?
(HE-LHC, 2030)

## Slide 11: HE-LHC 20-T hybrid magnet
Block layout of Nb-Ti & Nb3Sn & HTS (Bi-2212) 20-T dipole-magnet coil. Only one quarter of one aperture is shown.
E. Todesco,
L. Rossi,
P. McIntyre
A lot of stored energy in both magnets and beams!

## Slide 12: even stronger “magnets”? - crystals
W. Scandale, MPL A (2012)
l=2pb=2p (E/f)1/2
f~20-60 eV/Å2
crystal focusing strength
straight crystal
bent crystal
Bmax≈2000 T !
since 1978 crystals are used for extracting high-energy protons or ions from storage rings; can they by used for a circular collider? possible problems: “dechanneling” due to interactions w. crystal nuclei & e-; heating; staging – atomic-scale positioning?; synchrotron radiation
S.A. Bogacz, D. Cline, 1997

## Slide 13
p: not fundamental, made of partons
discovered in inelastic electron-nucleon scattering experiments at SLAC ESA,
1967-1973

## Slide 14
MIT-SLAC (1967-73)→ HERA (1990-2007) → LHeC (2025-32?)
6-pass 2x10-GeV recirculating linac with energy recovery
next step in ep scattering?

## Slide 15: lepton colliders
“precision instruments” (fundamental particles)
circular colliders
  - e+e-
  - m-m+
linear e+e- colliders
  - normal or superconducting m-wave linac
  - dielectric or plasma-based linac
  - crystal accelerator

## Slide 16: circular e+e- colliders
largest circular colliders:
highest energy: LEP (27 km), 104.5 GeV/beam
  → 80 km (“TLEP”?)
  another factor 2 in beam energy, 200 GeV
max. beam energy limited by synchr. radiation
Emax[100 GeV]≈(PSR[70MW] r2[km]/Ne[1012])1/4
SR power
~1/2 wall plug power
with 50% RF efficiency
bending radius
LHC: r≈3 km
#e±
(for luminosity)

## Slide 17: possible master plan
PSB
PS (0.6 km)
SPS (6.9 km)
LHC (26.7 km)
TLEP (80 km,
e+e-, up to
400 GeV c.m.)
L(350GeV)≈7x1033cm-2s-1
L(240GeV)≈1035cm-2s-1
L(160GeV)≈4x1035cm-2s-1
L(91GeV)≈3x1036cm-2s-1
VHE-LHC
(pp, up to
100 TeV c.m.)
Also: e± (200 GeV) – p (7 & 50 TeV) collisions
not yet endorsed by CERN management!

## Slide 18
maximum beam energy limited by n radiation
Emax[TeV]≈(D[mSv/y]L2[km]/(dNm/dt[1013/s])1/3
radiation dose / year
at distance L
distance
circular m+m- colliders
other issues:
m production, m cooling,
m acceleration, …
#m into collider / s
B. King, 1999
energy limited to a few TeV
synchrotron radiation smaller than for e± by factor (me/mm)4≈6x10-10

## Slide 19
max. beam energy limited by accel. gradient
Emax ≈ 1/3 G L
accelerating
gradient
total length
linear e+e- colliders
for example: L=30 km ; max G from surface breakdown
G=30 MV/m→ Emax≈ 300 GeV (SC RF)
G=100 MV/m (breakdown)→ Emax≈ 1 TeV (NC RF)
higher linear-collider energy needs higher gradients!
(dielectric, plasma, crystals … see later)
other issues:
luminosity, power, e+ production, spot sizes,
beamstrahlung (synchrotron radiation in collision),…

## Slide 20: example linear e+e- colliders
SLAC Linear Collider
(SLC) 1990-1998
the only linear collider
so far
proposed
future
linear
colliders
ILC (SC)
31 km
500 GeV c.m.
CLIC
(NC),
48 km
3 TeV
c.m.

## Slide 21
dielectric & plasma accelerators
dielectric materials (quartz, diamond, garnets,….)
higher breakdown limits than metals;
dielectric structures driven in THz,
optical or near-IR regime
G=1-3 GV/m
driven by e- beam or by laser (external fiber laser or
integrated semiconductor laser)
plasma acceleration
G≈ 100 GV/m (n0 [1018 cm-3])1/2 ; n0 ≈1017-1018 cm-3
driven by laser, e- beam, or p beam
Kostyukov, Nerush, Litvak, 2012
unlimited acceleration is predicted to be possible ?!

## Slide 22
crystal accelerators
acceleration in crystal channels
G≈ 10 TV/m (n0 [1022 cm-3])1/2 ; n0 ≈1022-1023 cm-3
driven by x-ray laser
max. energy set by radiation emission due to betatron oscillations between crystal planes
Emax ≈300 GeV for e+, 106 TeV for p ? Chen & Noble 1997; Dodin & Fisch 2008
[is there no similar limit for plasmas?]
10 TV/m – disposable crystal accelerator
or 0.1 TV/m – reusable crystal accelerator
side injection of x-ray pulses using long fibers

## Slide 23: far-reach future colliders
 | dielectric | plasma | crystal
accelerating media | micro-structures | ionized plasma | solid crystals
energy source option 1 option 2 option 3 | opt. laser e- bunch p bunch | e- bunch p bunch opt. laser | x-ray laser
preferred particles | any stable | e-, m- | p+, m+
max. accel. gradient | 1-3 GV/m | 30-100 GV/m | 0.1-10 TV/m
c.m. energy in 10 km | 3-10 TeV | 3-50 TeV | 103-105 TeV
#stages/10 km option 1 option 2 option 3 | 105-106 104-105 2-10 | ~100 103-104 2-102 | ~2
inspired by
V. Shiltsev, 2012,
Physics-Uspekhi

## Slide 24: towards shorter wavelengths
conventional
accelerators
dielectric & plasma
based accelerators
crystal accelerators
tetrodes, IOTs,
klystrons,
solid-state
amplifiers,…
e- (p) beam
or laser
intense X-ray
laser
accelerator
type
accelerator
power source

## Slide 25: highest-energy particles
4 July 2012 CERN, Geneva, Switzerland
Higgs boson – “God particle”? – mass 1.25x1011 eV, neither matter nor force!
15 October 1991 Dugway Proving Ground, Utah, U.S.A.
“Oh-my-God-particle”!
(kinetic) energy 3x1020 eV
(=3x1011 GeV = 300 EeV)!

## Slide 26: cosmic-ray energy spectrum
P. Blasi, UHECR2012
1045 m-2s-1sr-1GeV1.5!
LHC p energy
x108
GZK limit
dielectric & plasmas
crystal accelerator driven by X-ray laser

## Slide 27: SLAC is well positioned for the next 50 years!
many pioneering papers across the field
exceptional forward-looking facilities

## Slide 28: ultimate limit of electromagnetic acceleration
Ecr ≈1018 V/m critical field for e+e-
pair creation - ħ/(mec) e Ecr ~ mec2
reaching Planck scale of 1028 eV
would need 1010 m long accelerator
[1010 m= 1/10th of distance earth-sun]
“not an inconceivable task for an
advanced technological society”
P. Chen, R, Noble, SLAC-PUB-7402, April 1998

## Slide 29: step back to 2015-20

## Slide 30: Higgs production at hadron & lepton colliders
LHC
e+e- collider
Higgs-strahlung, dominant for ECoM<500 GeV

## Slide 31
“Higgs” strongly couples to gg
LHC CMS result
LHC ATLAS result

## Slide 32: a new type of collider?
g
g
H
t, W, …
gg collider Higgs factory
another advantage:
no beamstrahlung
→ higher energy reach
than e+e- colliders

## Slide 33: combining photon science & particle physics!
K.-J. Kim, A. Sessler
Beam Line
Spring/Summer 1996
gg collider
few J pulse
energy with
l~350 nm

## Slide 34
Source: Fiber Based High Power Laser Systems,
Jens Limpert, Thomas Schreiber, and Andreas Tünnermann
power evolution of cw double-clad
fiber lasers with diffraction limited
beam quality over one decade:
factor 400 increase!
laser progress: example fiber lasers

## Slide 35
passive optical cavity
→
relaxed
laser
parameters
K. Moenig et al, DESY Zeuthen

## Slide 36
self-generated FEL g beams
(instead of laser)?
optical
cavity
mirrors
wiggler
converting some
e- energy into
photons (l≈350 nm)
e-
(80 GeV)
e-
(80 GeV)
Compton
conversion
point
gg IP
e- bend
e- bend
example: lu=50 cm, B=5 T, Lu=50 m, 0.1%Pbeam≈25 kW
“intracavity powers at MW levels are perfectly reasonable” – D. Douglas, 23 August 2012

## Slide 37
SAPPHiRE: a Small gg Higgs Factory
SAPPHiRE: Small Accelerator for Photon-Photon Higgs production using Recirculating Electrons
scale ~ European XFEL,
about 10k Higgs per year

## Slide 38
would it fit on SLAC site?

## Slide 39
now is the time!

## Slide 40
SLAC’s particle accelerators have been at forefront of discoveries for 50 years
SLAC will be a strong player in the accelerator revolution of next 50 years;
no other lab can better push dielectric, plasma & x-ray crystal acceleration!
next SLAC machine - a Higgs factory?
HAPPY BIRTHDAY – SLAC !

## Slide 43
“SLAC reunion” at the harbour of San Sebastian on 6 September 2011